## Slide 1: Intrepid Device Protocol
Mark Menge
2/26/2024

## Slide 2: Protocol Details: Ethernet Header
Message | Description
Tx Summary (up to 1500 bytes) | [icsEthHdrTxRx(24 bytes)][Tx Command Header][message1][Tx Command Header][message2]...
Rx Summary (up to 1500 bytes) | [icsEthHdrTxRx(24 bytes)][Rx Command Header][message1][Rx Command Header][message2]...
Ethernet header | // Ethernet header struct icsEthHdrTxRx // 24 bytes. For both Tx and Rx { uint8_t destMAC[6]; // 0..5 uint8_t srcMAC[6]; // 6..11 uint16_t etherType; // 12..13 0xCAB1 host to device and CAB2 device to host // Big endian uint32_t icsEthernetHeader; // 0xaaaa5555 OK 14..17 // Big endian uint16_t payloadSize; // 18..19 little endian uint16_t packetNumber; // 20..21 little endian // packetInfo little endian uint16_t firstPiece : 1; // 22.0 uint16_t lastPiece : 1; // 22.1 uint16_t bufferHalfFull : 1; // 22.2 uint16_t unused: 5; // 22.3..6 uint16_t Protocol : 8; // 23 /* Payload starts now uint8_t AA; // AA marks the start of header */ };

## Slide 3: Protocol Details: Tx Commands - EtherType CAB1 [icsEthHdrTxRx(24 bytes)][Tx Command Header][message1] See LogTx()
icsAAUpdateLEDStateCmd *pOldCmd = (icsAAUpdateLEDStateCmd *)data;
icsAAShortHeaderCmd *pShortHeader = (icsAAShortHeaderCmd *)data;
icsAALongHeaderCmd *pLongHeader = (icsAALongHeaderCmd *)data;
if (pOldCmd->zero == 0 && pOldCmd->command == 6)// old command
use icsAAUpdateLEDStateCmd
return
else if (pShortHeader->packetLength) // short 2 byte header
use icsAAShortHeaderCmd, message is ics51CommandTx
return
else // 6 byte header
use icsAALongHeaderCmd message is one:
IcsCanPacket29Fd
IcsCanPacket11Fd
IcsCanPacket29
IcsCanPacket11

## Slide 4
Host Tx Message Examples | Description
(icsEthHdrTxRx(24 bytes)) [icsAAUpdateLEDStateCmd] or [icsAAShortHeaderCmd][IcsCanPacket11] [icsAAShortHeaderCmd][IcsCanPacket29] Or [icsAALongHeaderCmd][IcsCanPacket11] [icsAALongHeaderCmd][IcsCanPacket29] [icsAALongHeaderCmd][IcsCanPacket11Fd] [icsAALongHeaderCmd][IcsCanPacket29Fd] ics51CommandTx … | 

## Slide 5: Host Tx Command Headers
Host Tx Command | Description
icsEthCANTx | struct icsEthCANTx { icsEthHdrTxRx EthHdr;// 24 bytes icsAALongHeaderCmd Hdr;// 6 bytes union { IcsCanPacket11 Can11;// 14 IcsCanPacket29 Can29; IcsCanPacket11Fd Can11Fd; IcsCanPacket29Fd Can29Fd; }; };
icsAAUpdateLEDStateCmd | Update the LED struct icsAAUpdateLEDStateCmd { uint8_t AA;// 0 uint8_t networkID : 4;// 1.0..1.3 uint8_t packetLength : 4;// 1.4..1.7e uint8_t zero;// 2 zero uint8_t command;// 3 always 6 uint8_t LEDState;// 4 Offline = 0x04,CoreMiniRunning = 0x08, Online = 0x10 uint8_t checksum;// checksum };
icsAAShortHeaderCmd | struct icsAAShortHeaderCmd {// short 2 bytes uint8_t AA; uint8_t networkID : 4; uint8_t packetLength : 4; // The packet length given in short packets does not include header (must add 2). If 0, long packet type };
ics51CommandTx | struct ics51CommandTx {// ics51CommandTx uint8_t AA;// 0 uint8_t NetID : 4;// 1.0..3 uint8_t PacketSize : 4;// 1.4..7 uint8_t Command;// 2 eg A9 uint8_t Data[16];// 3 optional data, last byte is checksum };
icsAALongHeaderCmd | struct icsAALongHeaderCmd {// Host-To-Device long 6 bytes Intrepid calls this Main51 command uint8_t AA;// 0 uint8_t NetIDRed;// Sometimes C sometime B hmm uint16_t packetLength;// 2..3 union { uint8_t command; uint16_t networkID;// 4..5 }; };

## Slide 6: Host Tx Commands – 11 bit CAN
Host Tx Command | Description
IcsCan11BitArb | struct IcsCan11BitArb { uint8_t ArbID_3_11;// 0 uint8_t ArbID_0_2; // 1 int GetArbID() { return (ArbID_3_11 << 3) + (ArbID_0_2 >> 5); } int SetArbID(int ID) { ID = ID & 0x7FF; ArbID_0_2 = ID << 5; ArbID_3_11 = ID >> 3; return ID; } };
IcsCanPacket11 | struct IcsCanPacket11 // 14 bytes { uint8_t NetworkID : 4;// Network::NetID::Main51 whatever that means 0.0..3 uint8_t Size : 4;// DLC 0.4..7 uint16_t DescriptionID;// big endian 1..2 IcsCan11BitArb ArbID;// 3..4 uint8_t LengthNibble : 4;// 5.0..3 uint8_t statusNibble : 4;// 5.4..7 uint8_t data[8];// 6..13 };

## Slide 7: Host Tx Commands – 29 bit CAN
Host Tx Command | Description
IcsCan29BitArb | struct IcsCan29BitArb { uint8_t ArbID_28_21;// byte 0 uint8_t ArbID_16_17 : 2;// byte 1 uint8_t : 1; uint8_t b29 : 1;// if 1, then extended uint8_t : 1; uint8_t ArbID_18_20 : 3; uint8_t ArbID_8_15;// byte 2 uint8_t ArbID_0_7;// byte 3 int GetArbID() { return ArbID_0_7 + (ArbID_8_15 << 8) + (ArbID_16_17 << 16) + (ArbID_18_20 << 18) + (ArbID_28_21 << 21); } int SetArbID(int ID) { ID = ID & 0x1FFFFFFF; ArbID_0_7 = ID & 0xFF; ArbID_8_15 = (ID >> 8) & 0xFF; ArbID_16_17 = (ID >> 16) & 0x3; ArbID_18_20 = (ID >> 18) & 0x7; ArbID_28_21 = (ID >> 21) & 0xFF; return ID; } };
IcsCanPacket29 | struct IcsCanPacket29 // 29 bit { uint8_t NetworkID : 4;// 0 Network::NetID::Main51 uint8_t Size : 4; uint16_t DescriptionID;// 1..2 big endian¦ 1..2 IcsCan29BitArb ArbID;// 3..6¦ 3..6 uint8_t LengthNibble : 4;// 7.0..3 uint8_t statusNibble : 4;// 7.4..7 uint8_t data[8];// 8..15 };

## Slide 8: Host Tx Commands – 29 bit CAN FD
Host Tx Command | Description
IcsCanPacket29Fd | struct IcsCanPacket29Fd // 29 bit { uint8_t NetworkID : 4;// 0 Network::NetID::Main51 uint8_t Size : 4; uint16_t DescriptionID;// 1..2 big endian IcsCan29BitArb ArbID;// 3..6 uint8_t FDFrame;// = 0xF;// 7 uint8_t LengthNibble : 7;// 8.0..6 uint8_t BaudRateSwitch : 1; // 8.7AKA BRS, indicates FD? uint8_t data[64];// 9..72 };

## Slide 9: Protocol Details: Rx Messages - EtherType CAB2 Step 1 -Determine if short of long header Step 2 – Get Network ID Step 3 – Get Type of network ID [icsEthHdrTxRx(24 bytes)][Rx Command Header][Message1]... See LogRx()
icsAAShortHeaderRx *pShtPkt = (icsAAShortHeaderRx *)data;
icsAALongHeaderRx *pLongPkt = (icsAALongHeaderRx *)data;
if (pShtPkt->packetLength)
NetID = (icsneo::NetID::NetID)pShtPkt->networkID; // 2 byte short header
else
NetID = (icsneo::NetID::NetID)pLongPkt->networkID;// 6 byte long header
NetType = icsneo::GetTypeOfNetID(NetID);
switch NetType:
case icsneo::NetID::Device:
case icsneo::NetID::DeviceStatus:
case icsneo::NetID::ReadSettings:// 0x3C
case icsneo::NetID::Reset_Status:// 0x36
case icsneo::NetID::RED_OLDFORMAT://0x25:
if (cmd == RequestSerialNumber)
else if (cmd == GetMainVersion)
else if (cmd == GetSecondaryVersions)
case icsneo::NetID::Main51:
case RequestSerialNumber:
ptr += sprintf(ptr, "%s", SerialNumToString(*(uint32_t *)(data + 1)));
case icsneo::Type::CAN:
ptr += DecodeCANMessageRx(ptr, pHwCanPkt);
case icsneo::Type::Ethernet:
case icsneo::Type::Other:

## Slide 10: Device Message Headers
icsAAShortHeaderRx | struct icsAAShortHeaderRx {// short 2 bytes uint8_t AA; uint8_t networkID : 4; uint8_t packetLength : 4; // The packet length given in short packets does not include header (must add 2). If 0, long packet type };
icsAALongHeaderRx | struct icsAALongHeaderRx {// long 6 bytes uint8_t AA;// 0 uint8_t networkIDZero : 4;// 1.0..1.3 uint8_t packetLengthZero : 4;// 1.4..1.7. if 0, then long packet type uint16_t packetLength;// 2..3 uint16_t networkID;// 4..5 icsneo::Type::Type GetType() { return icsneo::GetTypeOfNetID((icsneo::NetID::NetID)networkID); } };

## Slide 11: Device CAN Messages
HardwareCANPacket | 
HardwareCANPacket | struct HardwareCANPacket {// used as bitfield! 24 bytes struct { icscm_bitfield IDE : 1; icscm_bitfield SRR : 1; icscm_bitfield SID : 11; icscm_bitfield EDL : 1; icscm_bitfield BRS : 1; icscm_bitfield ESI : 1; } header; struct { icscm_bitfield EID : 12; icscm_bitfield TXMSG : 1; icscm_bitfield TXAborted : 1; icscm_bitfield TXLostArb : 1; icscm_bitfield TXError : 1; } eid; struct { icscm_bitfield DLC : 4; icscm_bitfield RB0 : 1; icscm_bitfield IVRIF : 1; icscm_bitfield HVEnable : 1;// must be cleared before passing into CAN driver icscm_bitfield ExtendedNetworkIndexBit : 1;//DO NOT CLOBBER THIS icscm_bitfield RB1 : 1; icscm_bitfield RTR : 1; icscm_bitfield EID2 : 6; } dlc; unsigned char data[8]; uint16_t stats; struct { uint64_t TS : 60; uint64_t : 3; // Reserved for future status bits uint64_t IsExtended : 1; } timestamp; // unsigned char FdData[64]; Fd data is reported after this structure int GetArbID(); bool Is29BitArbID() { return header.IDE; } bool IsFD() { return header.EDL && timestamp.IsExtended; } int GetDataLength() { return CANFD_DLCToLength(dlc.DLC); } };

## Slide 12: Summary
Start a new github project with simplified code
Easier to port to other OS’s
Easier to understand and debug